## Slide 1
Object-Oriented Programming
Programming Project #1
郭建志

## Slide 2: Background
Wireless ad hoc network without GPS
Every node only has the local information (i.e., its neighbors’ information) and the destination’s information
source
destination

## Slide 3: Background
Wireless ad hoc network without GPS
Every node only has the local information (i.e., its neighbors’ information) and the destination’s information
source
destination

## Slide 4: Naïve Routing Scheme: AODV (BFS)
AODV: ad hoc on-demand distance vector routing
Broadcast RREQ from the source to all nodes
Each node records the hop distance to the source
Send RREP from the destination to the source along the path
source
destination
1
1
1
1
2
2
1
2
2
3
3
3
3
3
4
4
4
4
5
5
5
6
6
6
6
7
7

## Slide 5: Naïve Routing Scheme: AODV (BFS)
AODV: ad hoc on-demand distance vector routing
Broadcast RREQ from the source to all nodes
Each node records the hop distance to the source
Send RREP from the destination to the source along the path
source
destination
1
1
1
1
2
2
1
2
2
3
3
3
3
3
4
4
4
4
5
5
5
6

## Slide 6: Naïve Routing Scheme: AODV (BFS)
AODV: ad hoc on-demand distance vector routing
Advantage: Shortest path guaranteed
Disadvantage: Broadcast storm problem Scalability issue
source
destination
1
2
3
4
5
6

## Slide 7: Routing Tables of Nodes for AODV
Every node has a routing table
For example, the table of node 0 is
Destination | Next
2 | 6
4 | 9
… | …
0
9
6
2
4

## Slide 8: Programming Project #1: AODV
Input:
  Number of nodes and links
  A set of nodes and a set of links
  Routing pairs (source, destination)
Procedure:
  Broadcast from the source
  Construct the routing table in each node
  Build a routing path from destination
Output:
  Routing paths

## Slide 9: Programming Project #1: AODV
Requirement:
  RREQ is sent toward the node with a smaller ID if there are multiple nodes with the same hop count
  Construct the routingTable before routing
  class node { public: unsigned int sendTo (int dstID); // return next private: <any type> routingTable; unsigned int id; }
  node *sensor = new [num]; unsigned cur_id = srcID; while (cur_id != dstID){ cur_id = sensor[cur_id].sendTo(dstID); }

## Slide 10: Input Sample: request.txt
Format:
#nodes #undirectedLinks
linkID firstNodeID secondNodeID
…
#requestFlows
flowID sourceID destinationID
…
下次揭曉，先自己設計input

## Slide 11: Output Sample: result.txt
Format:
flowID firstNode secondNode … lastNode
…
下次揭曉，用自己設計input產生答案

## Slide 12: Input Sample: std cin
Example:
6 8
0 0 1
1 0 3
2 1 3
3 1 5
4 2 3
5 2 4
6 2 5
7 4 5
4
0 0 4
1 3 5
2 2 0
3 4 0
0
1
3
5
4
2
1
1
2
2
3

## Slide 13: Input Sample: std cout
input:
…
4
0 0 4
1 3 5
2 2 0
3 4 0
destination | next
4 | 3
0
1
3
5
4
2
destination | next
4 | 4
output:
0 0 3 2 4
1 3 1 5
2 2 3 0
3 4 5 1 0
destination | next
4 | 2
1
1
2
2
3

## Slide 14: Input Sample: std cout
input:
…
4
0 0 4
1 3 5
2 2 0
3 4 0
destination | next
1 | 1
2 | 3
3 | 3
4 | 3
5 | 1
destination | next
0 | 0
2 | 3
3 | 3
4 | 5
5 | 5
destination | next
0 | 5
1 | 5
2 | 2
3 | 2
5 | 5
0
1
3
5
4
2
destination | next
0 | 3
1 | 3
3 | 3
4 | 4
5 | 5
destination | next
0 | 1
1 | 1
2 | 2
3 | 1
4 | 4
output:
0 0 3 2 4
1 3 1 5
2 2 3 0
3 4 5 1 0
destination | next
0 | 0
1 | 1
2 | 2
4 | 2
5 | 1

## Slide 15: Input Sample: std cout
input:
…
4
0 0 4
1 3 5
2 2 0
3 4 0
destination | next
1 | 1
2 | 3
3 | 3
4 | 3
5 | 1
destination | next
0 | 0
2 | 3
3 | 3
4 | 5
5 | 5
destination | next
0 | 5
1 | 5
2 | 2
3 | 2
5 | 5
0
1
3
5
4
2
destination | next
0 | 3
1 | 3
3 | 3
4 | 4
5 | 5
destination | next
0 | 1
1 | 1
2 | 2
3 | 1
4 | 4
output:
0 0 3 2 4
1 3 1 5
2 2 3 0
3 4 5 1 0
destination | next
0 | 0
1 | 1
2 | 2
4 | 2
5 | 1

## Slide 16: Note
神人期限(分數=100): 3/31 Tue (待調整)
繳交期限(分數上限90): 4/7 Tue (待調整)
超過一天扣 10 分
上傳 E-course2
C++ Source code
Show a good programming style